## Slide 1: Comparing Network Cables
Computer Networking

## Slide 2: Comparing Network Cables
The Internet uses three main types of cable to transfer data between computers.
  UTP (unshielded twisted pair),
  coaxial, and
  fiber optic.
  Both UTP and coaxial cables transmit information
  using electrical signals; fiber optic cables use pulses
  of light to send information.

## Slide 3: Unshielded Twister Pair (UTP) Cable
Home and businesses use UTP cable to connect computers over short distances, up to the size of a football field (100 meters).
Networks assembled with twisted-pair cables can connect computers with intermediary devices.
There are some issues with Electromagnetic interference (EMI).
Notes: UTP cable is also the most common cable used in computer networking. Modern Ethernet, the most common data networking standard, utilizes UTP cables. Twisted pair cabling is often used in data networks for short and medium length connections because of its relatively lower costs compared to optical fiber and coaxial cable.
Twisted pair cabling is a type of wiring in which two conductors of a single circuit are twisted together for the purposes of canceling out electromagnetic interference (EMI) from external sources; for instance, electromagnetic radiation from unshielded twisted pair (UTP) cables, and crosstalk between neighboring pairs. It was invented by Alexander Graham Bell.

## Slide 4: Unshielded Twisted Pair

## Slide 5: Categories of Unshielded Twisted Pair
Type | Frequency | Use (speed in Megabits per second)
Category 5e | 100 MHz | data to 1,000 Mbps (Gigabit Ethernet)
Category 6 | 250 MHz | data to 1,000 Mbps (Gigabit Ethernet)
Category 6a | 500 MHz | data to 10,000 Mbps (10 Gigabit Ethernet)
Category 7 | 600 MHz | data to 10,000 Mbps (10 Gigabit Ethernet)
Category 7a | 1000 MHz | data to 10,000 Mbps (future standard)
The following table compares the speeds in megabits per second and minimum frequencies in megahertz of different categories of UTP cable.

## Slide 6: Coaxial Cable
Notes: Plastic Jacket
Metallic Shield
Dielectric Insulator
Center Core

## Slide 7: Coaxial Cable

## Slide 8: Coaxial Cable

## Slide 9: Fiber-Optic Cable
Contains strands of glass or plastic that transmit light rather than electrical signals, and they are coated in Kevlar and plastic.
http://en.wikipedia.org/wiki/Optical_fiber

## Slide 10: Assignment
Create a table of the three types of network cables that shows how each is made, how it is used in networking and the features and benefits:
Type of Cable | Description | Use | Benefits/ Disadvantages
UTP |  |  | 
coaxial |  |  | 
Fiber optic |  |  |